## Slide 1: Qiskit Pulse
a Framework for Pulse-Level Control

## Slide 2: Intro to Qiskit Pulse
Qiskit Circuit model – abstraction that hides the gates’ nature
Qiskit Pulse – provides pulse-level control of IBM quantum systems
  Pulses are discrete time-series of amplitudes

## Slide 3: Comparison between Circuit and Pulse-Level Control
Qiskit Circuit model
High-level abstraction
Uses gates as building blocks
  Gates are pre-calibrated
Saves time from calibration
Limits access to hardware
Uses first two energy levels only
Qiskit Pulse
Low-level framework
Uses discrete time-series (pulses) as building blocks
  One time unit ( ns) is the lowest-level unit
Allows for fine control of IBM quantum systems
Can use more than two energy levels

## Slide 4: How to make the quantum gates?
Qiskit Circuit model uses two levels for the gates – and
Gates – time evolution operators with different acting for time
Let’s use 2 energy levels only as in circuit model

## Slide 5: Time Evolution Operator
In the Rabi model and are constant, thus

## Slide 6: Time Evolution Operator
Taking only
We find the transition probability
And in resonance () we have
If the pulse is not constant, the cosine argument becomes the pulse area

## Slide 7: Demonstration of Rabi Oscillations
Maximas are at pulse areas that are odd multiples of (, , …)
Minimas are at even multiples of (, , …)

## Slide 8
Pulse with area transfers half of the population to the excited state.
Pulse with area transfers the whole population to the excited state.
But… how to make a Hadamard gate??
Common gates in Qiskit Pulse

## Slide 9: How to make a Hadamard?
Sqrt of X gate similarly transfers half of population to excited state
But , while
In 2-level system only possible with non-zero detuning

## Slide 10: Choose Detuning for Hadamard
Do a frequency sweep around resonant frequency
Find the amplitude
Find the detuning for which the transition probability is half the maximum
This is the detuning that should be used for the Hadamard gate

## Slide 11: Pulse Basics
Learn how to build and apply pulses

## Slide 12: Qubit Calibration
Learn how to calibrate the qubit for further use

## Slide 13: 1st Step: Calibration of Resonant Frequency
We use a built-in estimation of the qubit resonant frequency
Play the same pulse with different driving frequency sweeping around the given frequency
Plot the transition probability for each frequency

## Slide 14: 1st Step: Calibration of Resonant Frequency
4. Fit the resonance curve with a type of convex symmetric function (most often Lorentzian)
5. Take the parameters of the fit to find a value for the resonant frequency

## Slide 15: 2nd Step: Calibration of Pulse Area
Using the previously found resonant frequency, conduct experiments with 1 pulse each
Apply a pulse of any shape while increasing the amplitude (Rabi frequency) with each test
Plot the transition probability (equiv. signal) for each amplitude

## Slide 16: 2nd Step: Calibration of Pulse Area
4. Fit the resulting curve with a cosine function
5. Use the parameters to find the first maximum of the function (corresponding to pulse area )
Your pulse is ready (equiv. to an X gate)

## Slide 17: 3rd Step: Discriminator
Optional, because we can use a built-in Qiskit discriminator for 2 states only
The raw result from the experiment is a complex signal
  One cannot differentiate the state of the particle directly
Classification of the measured signals is necessary

## Slide 18: 3rd Step: Build a Discriminator
Conduct three repeated experiments:
  An empty circuit that yields (predominantly) the state
  Circuit with one pulse with frequency of that yields (predominantly) the state
Measure the signals and plot them on two-dimensional graph – with the axes corresponding to the real and imaginary part of the signal

## Slide 19: Qiskit Pulse: Freedom to Customize Your Experiments in Numerous Ways
You can:
Access higher energy states
Apply pulses with custom waveforms (i.e. Gaussian, etc.)
Not change the detuning during the circuit execution, BUT…
  Can apply complex Rabi frequencies which effectively create a detuning

## Slide 20: the 3rd Energy Level
Learn how to access and use the 3rd energy state

## Slide 21: Accessing the 3rd Energy Level
The procedure is analogous to the procedure for the first 2 states
There are 2 ways to excite population to the 3rd level:
  Make a pulse with
Biggest difference – a discriminator is not available
  Can be built by you

## Slide 22: Build a Discriminator
Conduct three repeated experiments:
  An empty circuit that yields (predominantly) the state
  Circuit with one pulse with frequency of that yields (predominantly) the state
  Circuit with one pulse with frequency of followed by a pulse with the frequency of that yields (predominantly) the state
Measure the signals and plot them on two-dimensional graph – with the axes corresponding to the real and imaginary part of the signal
Use a model to find a separation line (e.g. Linear Discriminant Analysis)

## Slide 23: The Discriminator
The division between states and is not very clear
  Introduces a bigger error
The discriminator is not a line anymore

## Slide 24: Any Questions?